IBT 300

Fisier  isdn_s0.mon

SETUP

I Frame SAPI=0  TEI=75 N(R)=0  N(S)=0

Call Reference:

Flag : Call Origin Side

Len : 1

Value : 0xA

Protocol Discriminator : 08

SETUP

BEARER CAPABIL.  Lg = 3

Hex. Value :		90 90 A3

Coding stand. :	CCITT coding

Info tr. Capab. :	3,1 KHz audio

Transfer mode :	circuit mode

Info tr. rate :		64 kbit/s

Layer 1 ident.

User info L 1 		Rec. G.711 Alaw

CALLING PARTY NB 	Lg = 11

Hex. Value : 		80 30 32 39 39 31 32 35 31 30 34

Type of numb. :	unknown

Number plan. :	unknown

No. Digit/IA5	:	0299125104

HIGH LAYER COMP 	Lg = 2

Hex. Value : 		91 01

Coding stand. :	CCITT coding

Interpretat		st. HL id. Used

Present meth.

High layer protocol profile

High layer charact. Identific. Telephony

SETUP ACK.

I Frame SAPI=0  TEI=75 N(R)=1 N(S)=0

Call Reference:

Flag : Call Receiver Side

Len : 1

Value : 0xA

Protocol Discriminator : 08

SETUP ACK

CHANNEL IDENT.		Lg = 1

Hex. Value		89

Chan. Select.:		B1 channel

Exclusive

Net. D channel

Int. Implicitly

CALL PROCEEDING

I Frame SAPI=0  TEI=75 N(R)=1  N(S)=1

Call Reference:

Flag : Call Receiver  Side

Len : 1

Value : 0xA

Protocol Discriminator : 08

CALL PROC.

CHANNEL IDENTI.		Lg = 1

Hex. Value		89

Chan. Select.:		B1 channel

Exclusive

Net. D channel

Int. Implicitly

SETUP

I Frame SAPI=0  TEI=127

Call Reference:

Flag : Call Origin Side

Len : 1

Value : 0x25

Protocol Discriminator : 08

SETUP

BEARER CAPABIL.  Lg = 3

Hex. Value :		90 90 A3

Coding stand. :	CCITT coding

Info tr. Capab. :	3,1 KHz audio

Transfer mode :	circuit mode

Info tr. rate :		64 kbit/s

Layer 1 ident.

User info L 1 		Rec. G.711 Alaw

CHANNEL IDENT		Lg =1

Hex. Value		8A

Chan. Select.:		B2 channel

Exclusive

Net. D channel

Int. Implicitly

CALLING PARTY NB 	Lg = 11

Hex. Value : 		20 83 32 39 39 31 32 35 31 30 34

Type of numb. :	national

Number plan. :	unknown

Present indic.		Allows

Screening ind.		NT provided

No. Digit/IA5	:	0299125104

CALLED PARTY NB 	Lg = 5

Hex. Value : 		01 35 31 30 34

Type of numb. :	unknown

Number plan. :	ISDN/telephony

No. Digit/IA5	:	5104

HIGH LAYER COMP 	Lg = 2

Hex. Value : 		91 01

Coding stand. :	CCITT coding

Interpretat		st. HL id. Used

Present meth.

High layer protocol profile

High layer charact. Identific. Telephony

ALERTING

I Frame SAPI=0  TEI=75   N(R)=2  N(S)=1

Call Reference:

Flag : Call Receiver  Side

Len : 1

Value : 0x25

Protocol Discriminator : 08

ALERTING

CHANNEL IDENTI.		Lg = 1

Hex. Value		8A

Chan. Select.:		B2 channel

Exclusive

Net. D channelo

Int. Implicitly

CONNECT

I Frame SAPI=0  TEI=75   N(R)=2  N(S)=2

Call Reference:

Flag : Call Receiver  Side

Len : 1

Value : 0x25

Protocol Discriminator : 08

CONNECT

ALERTING

I Frame SAPI=0  TEI=75   N(R)=3  N(S)=2

Call Reference:

Flag : Call Receiver  Side

Len : 1

Value : 0xA

Protocol Discriminator : 08

ALERTING

CONNECT

I Frame SAPI=0  TEI=75   N(R)=3  N(S)=3

Call Reference:

Flag : Call Receiver  Side

Len : 1

Value : 0xA

Protocol Discriminator : 08

CONNECT

CONNECT ACK

I Frame SAPI=0  TEI=75   N(R)=3  N(S)=4

Call Reference:

Flag : Call Origin Side

Len : 1

Value : 0x25

Protocol Discriminator : 08

CONNECT ACK

INFORMATION

I Frame SAPI=0  TEI=75   N(R)=3  N(S)=5

Call Reference:

Flag : Call Receiver  Side

Len : 1

Value : 0xA

Protocol Discriminator : 08

INFORMATION

NETWORK SPC. FAC  	Lg = 7

Hex. Value : 		00 32 33 2A 01 00 00

Network specific facility

Hex. 			33 2A 01 00 00

INFORMATION

I Frame SAPI=0  TEI=75   N(R)=6  N(S)=3

Call Reference:

Flag : Call Origin  Side

Len : 1

Value : 0xA

Protocol Discriminator : 08

INFORMATION

NETWORK SPC. FAC  	Lg = 1

Hex. Value :		31

IA-5			  1

INFORMATION

I Frame SAPI=0  TEI=75   N(R)=6  N(S)=4

Call Reference:

Flag : Call Origin  Side

Len : 1

Value : 0xA

Protocol Discriminator : 08

INFORMATION

NETWORK SPC. FAC  	Lg = 1

Hex. Value :		32

IA-5			  2

DISCONNECT

I Frame SAPI=0  TEI=75   N(R)=6  N(S)=5

Call Reference:

Flag : Call Receiver  Side

Len : 1

Value : 0x2A

Protocol Discriminator : 08

DISCONNECT

CAUSE	Lg =2

Hex. Value		80 90

Coding stand. : 	CCITT

Location :		user

Cause class		normal

Normal call clearing

DISCONNECT

I Frame SAPI=0  TEI=75   N(R)=6  N(S)=6

Call Reference:

Flag : Call Receiver  Side

Len : 1

Value : 0x25

Protocol Discriminator :	 08

DISCONNECT

CAUSE			Lg =2

Hex. Value		87 90

Coding stand. : 	CCITT

Location :		internat netw

Cause class		normal

Normal call clearing

RELEASE

I Frame SAPI=0  TEI=75   N(R)=7  N(S)=6

Call Reference:

Flag : Call Receiver  Side

Len : 1

Value : 0x25

Protocol Discriminator : 	08

RELEASE

CAUSE			Lg =2

Hex. Value		80 90

Coding stand. : 	CCITT

Location :		user

Cause class		normal

Normal call clearing

REL COMP.

I Frame SAPI=0  TEI=75   N(R)=7  N(S)=7

Call Reference:

Flag : Call Origin Side

Len : 1

Value : 0x25

Protocol Discriminator : 08

REL COMPLETE

RELEASE

I Frame SAPI=0  TEI=75   N(R)=8  N(S)=7

Call Reference:

Flag : Call Receiver  Side

Len : 1

Value : 0xA

Protocol Discriminator : 	08

RELEASE

NETWORK SPC. FAC 	Lg=7

Hex. Value		00 32 34 2A 01 00 00

Network specific facility

Hex.			34 2A 01 00 00

NETWORK SPC. FAC 	Lg=7

Hex. Value		00 43238 2A 00 00 00

Network specific facility

Hex.			38 2A 00 00 00

REL COMP.

I Frame SAPI=0  TEI=75   N(R)=9  N(S)=7

Call Reference:

Flag : Call Origin Side

Len : 1

Value : 0xA

Protocol Discriminator : 08

REL COMPLETE

CAUSE			Lg =2

Hex. Value		80 90

Coding stand. : 	CCITT

Location :		user

Cause class		normal

Normal call clearing